## Slide 1: Hands-on Session
Xiaochen Hao, Ruifan Xu, Kexing Zhou, Youwei Xiao, Zizhang Luo, Fan Cui

## Slide 2: Setup
A: Download the docker image
  Please follow the handout or our website
  https://ericlyun.me/tutorial-aspdac2025
B: Login our server
  First, you need a SSH key
  check if your SSH directory exists
    win: C:\Users\<username>/.ssh
    linux: $HOME/.ssh
    mac: /Users/<username>/.ssh
  if not exists, you need to create one
    reference link
# Windows, open PowerShell
ssh-keygen -t ed25519 -C "<email>"
# Linux, open terminal
ssh-keygen -t ed25519 -C "<email>"
# Mac, open terminal
ssh-keygen -t ed25519 -C "<email>"
SSH public key can be found in <SSH>/id_ed25519.pub

## Slide 3: Setup
A: Download the docker image
  Please follow the handout or our website
  https://ericlyun.me/tutorial-aspdac2025
B: Login our server
  https://ahs.ericlyun.me
  User: ahs-aspdac25
  Pass: AgileChipDesign
  Enter your name and ssh key
  Follow the output to connect

## Slide 4: Setup
A: Download the docker image
  Please follow the handout or our website
  https://ericlyun.me/tutorial-aspdac2025
B: Login our server
  You can use PowerShell/terminal
  Or, you can use VSCode
    Ctrl-Shift-P / ⇧⌘P, type Remote: Show Remote Menu
      select SSH to install the extension
    Ctrl-Shift-P / ⇧⌘P, type Remote-SSH: Add New SSH Host
      paste “ssh root@ahs.ericlyun.me –p xxxxx”
    Ctrl-Shift-P / ⇧⌘P, type Remote-SSH: Connect to Host
    Ctrl-K + Ctrl-O, open /root/repos folder (optional: download rust-analyzer extension)

## Slide 5: Multi-level IR and debugger for HLS
Speaker: Xiaochen Hao, Ruifan Xu
郝晓辰 徐瑞帆

## Slide 6: What You Will Learn
Multi-level IR infrastructure
  Learn key concepts of our DSL and IR infrastructure
Systolic array generation
  Learn how to build a systolic array through dataflow representation and loop transformations
High-level synthesis and debugger
  Learn hardware generation and debugging mechanism

## Slide 7: Synthesis Flow
SCF IR
Tensor DSL
Tensor IR
GEMM, GEMV, DOT, GBMV, SYMV…
General Language
Software
IR
Structural
Representation
Scheduling
Representation
ToR IR
HEC IR
Verilog
Hardware
IR
Control flow
Representation

## Slide 8: Quick Try
Run:
bash ./hls-tutorial.sh generate
cd popa/examples
Then you will get:
Specification
(tutorial.cpp)
Tensor IR file
(exp_[0-3]])
// Only contains algorithm definition
Func exp_0(Buffer<int> &A,
Buffer<int> &B)
// Dataflow optimization applied
Func exp_3(Buffer<int> &A,
Buffer<int> &B)
SCF IR file
(mm_[0-3].mlir)

## Slide 9: Domain-specific Language (DSL)
Let us look at:
Buffer<float> A(N, M), B(S, N);
Var i("i"), j("j");
RDom k(0, N, "k");
Func C(Place::Device);
C(j, i) = sum(A(k, i) * B(j, k));
C.set_bounds(i, 0, M,
j, 0, S);
Target target = get_host_target();
target.set_feature(Target::MLIR);
C.compile_to_device(“SCF_vanilla.mlir”, {}, target);
Specification
(Func exp_0,
popa/examples/tutorial.cpp)
Declare input buffers
Declare loop variables (k is an reduction loop)
Define computations in a functional expression
Specify loop schedules
(How to optimize the computations)
Let us target MLIR

## Slide 10: IR Lowering
for (C.s0.i, 0, 16) {
for (C.s0.j, 0, 16) {
allocate sum[float32 * 1]
produce sum {
sum[0] = 0.000000f
for (sum.s1.k$x, 0, 16) {
sum[0] = sum[0] + (image_load("A",…) *image_load("B",…))
}
}
consume sum {
image_store("C", …, sum[0])
}
}
}
Tensor IR File
(popa/examples/exp_0)
Lowered SCF IR File
(popa/examples/mm_0.mlir)
affine.for %arg0 = 0 to 16 {
affine.for %arg1 = 0 to 16 {
%alloc_2 = memref.alloc()
memref.store %c0_i32, %alloc_2[%c0]
affine.for %arg2 = 0 to 16 {
%1 = affine.load %alloc_0[%arg1, %arg2]
%2 = affine.load %alloc[%arg2, %arg0]
%3 = arith.muli %2, %1
%4 = memref.load %alloc_2[%c0]
%5 = arith.addi %4, %3
memref.store %5, %alloc_2[%c0]
}
%0 = memref.load %alloc_2[%c0]
affine.store %0, %alloc_1[%arg1, %arg0]
}
}
Lowering
Loop structure:
tiling, unrolling, vectorization…
Statement: storage flattening, loop invariant hoisting…

## Slide 11: Systolic Array
How to build a systolic array?
Uniform Recurrence Equation (URE)
Space-time Transform (STT)
Dataflow
Software World
Temporal instruction pipeline
Load-store data access…
Hardware World
Spatial processing elements
Direct data propagation…
matmul
Dataflow Representation
Dataflow definition and mapping
Tiling
Vectorization
Systolic Array
Loop Transformation
Resource efficiency
(Func exp_[0-3], popa/examples/tutorial.cpp)

## Slide 12: A dataflow of matrix multiply
…
ij(k-1)
ij0
cij (0)
aik is not related with j. So reuse aik along dimension j
bkj is not related with i. So reuse bkj along dimension i
Reduce cij (from 0) along dimension k
ijk
Legend:
Iteration indexed by i, j, k
…
aik
ijk
i(j-1)k
i0k
bkj
(i-1)jk
0jk
…

## Slide 13: How to express the dataflow
Xijk = aik if j=0, Xi(j-1)k otherwise
Zijk = 0 if k=0, Zij(k-1)+Xijk Yijk otherwise
Yijk = bkj if i=0, Y(i-1)jk otherwise
Final result: Zijk if k reaches its max
Each loop iteration is associated with unique variables:
UREs
Xi(j-1)k
Xi0k
Xijk
Yijk
Y(i-1)jk
Y0jk
Zij(k-1)
Zijk
Zij0
…
aik
ijk
i(j-1)k
i0k
ij(k-1)
ij0
cij (0)
bkj
(i-1)jk
0jk
…

## Slide 14: How to express the dataflow
Xijk = aik if j=0, Xi(j-1)k otherwise
Zijk = 0 if k=0, Zij(k-1)+Xijk Yijk otherwise
Yijk = bkj if i=0, Y(i-1)jk otherwise
Final result: Zijk if k reaches its max
Each loop iteration is associated with unique variables:
UREs
X(k, j, i) = select(j == 0, A(k, i), X(k, j-1, i));
Y(k, j, i) = select(i == 0, B(j, k), Y(k, j, i-1));
Z(k, j, i) = select(k == 0, 0, Z(k-1, j, i)) + X(k, j, i) * Y(k, j, i);
C(j, i) = select(k == K-1, Z(k, j, i));
Specification
select(condition, x, y) = (condition ? x : y)
Uniform Recurrence Equations (UREs):
Recursive relationship
Uniform dependency
Dynamic single assignment form

## Slide 15: How to express the dataflow
Xijk = aik if j=0, Xi(j-1)k otherwise
Zijk = 0 if k=0, Zij(k-1)+Xijk Yijk otherwise
Yijk = bkj if i=0, Y(i-1)jk otherwise
UREs
for (i = 0; i < I; i++)
for (j = 0; j < J; j++)
for (k = 0; k < K; k++)
X(k, j, i) = …
Y(k, j, i) = …
Z(k, j, i) = …
C( j, i) = …
Initial IR
Dataflow mapping
PE
PE
PE
PE
j
i
Forming loop nest
  Each URE is defined within a separate iteration space
  Group them together under the same loop nest
Specification
…
X.merge_ures(Y, Z, C)
Put the UREs Y, Z, C in order, into the loop nest of X

## Slide 16: Dataflow Mapping
Space-time Transform
  Mapping loop instances onto spatial PEs
  Schedule instance execution in a temporal order
Scheduling vector：
Schedule point at time
Projection matrix:
Map point to
Map each point to a new space of
Space
Time

## Slide 17: Dataflow Mapping
(0, 0)
(0, 1)
(0, 2)
(1, 0)
(1, 1)
(1, 2)
(2, 0)
(2, 1)
(2, 2)
PE Array
a00
b02
b01
b00
a10
a20
k=0
k=0
k=0
a01
a02
a11
k=1
k=1
k=2
b10
b11
b20
PE(0,0) t=0:
Map a00->X000, b00->Y000, 0->Z000
PE(0,0) t=1:
Map a01->X001, b10->Y001, Z000->Z001
Map X000->X010 (reuse of a00 )
Map Y000->Y100 (reuse of b00 )
PE(0,0) t=2:
Map a02->X002, b20->Y002, Z001->Z002
Map X001->X011 (reuse of a01 )
Map Y001->Y101 (reuse of b10 )
Space-time Transform
  Mapping loop instances onto spatial PEs
  Schedule instance execution in a temporal order

## Slide 18: Dataflow Mapping
Specify space-time transform
Specification
…
X.space_time_transform(j, i)
Specification (Equivalent version)
X.space_time_transform({k, j, i}
{t, y, x},
{1, 1, 1,
0, 1, 0,
0, 0, 1})
  Scheduled STT:
Source loops
Destination loops
Projection matrix
Scheduling vector
  Unscheduled STT:
Specify only space loops

## Slide 19: Dataflow Mapping
Keeping input A stationary
  space_time_transform(k, i)
Exploring dataflow designs using space-time transform
Keeping input B stationary
  space_time_transform(k, j)
(0, 0)
(0, 1)
(0, 2)
(1, 0)
(1, 1)
(1, 2)
(2, 0)
(2, 1)
(2, 2)
PE Array
c00
a02
a01
a00
(0, 0)
(0, 1)
(0, 2)
(1, 0)
(1, 1)
(1, 2)
(2, 0)
(2, 1)
(2, 2)
PE Array
c00
b20
b10
b00
c10
c20
c10
c20

## Slide 20: Compilation
IR transformation and code generation
…
realize X.shreg[0, 16], [0, 16] {
unrolled for (X.s0.i, 0, 16) {
unrolled for (X.s0.j, 0, 16) {
pipelined for (X.s0.k, 0, 16) {
write_shift_reg("X.shreg", X.s0.j, X.s0.i,
select(X.s0.j == 0, image_load("A",…),
read_shift_reg("X.shreg", X.s0.j-1, X.s0.i)))
write_shift_reg("Y.shreg",…)
write_shift_reg("Z.shreg",…)
}
image_store("C", …)
}
}
}
Tensor IR
Lowered SCF IR
…
%alloc_4 = memref.alloc() : memref<16x16xi32>
affine.for %arg0 = 0 to 16 {
affine.for %arg1 = 0 to 16 {
affine.for %arg2 = 0 to 16 {
%1 = affine.load %alloc_4[%arg1 - 1, %arg0]
%2 = affine.load %alloc[%arg2, %arg0]
%5 = arith.select %4, %2, %1
affine.store %5, %alloc_4[%arg1, %arg0]
…
} {pipeline = 1}
%0 = affine.load %alloc_2[%arg1, %arg0]
affine.store %0, %alloc_1[%arg1, %arg0]
} {unroll = 0}
} {unroll = 0}
Loop annotation
Mapped Dataflow

## Slide 21: Tiling
Scaling to large matrices
  Partition the output matrix into tiles
  Compute tile-by-tile using a systolic array
PE
PE
PE
PE
X.space_time_transform(jj, ii)
for (X.s0.i, 0, 8) {
for (X.s0.j, 0, 8) {
pipelined (X.s0.k, 0, 16) {
unrolled (X.s0.ii, 0, 2) {
unrolled (X.s0.jj, 0, 2) {
write_shift_reg("X.shreg", …, read_shift_reg("X.shreg", X.s0.jj + -1, X.s0.ii))
write_shift_reg("Y.shreg", …, read_shift_reg("Y.shreg", X.s0.jj, X.s0.ii + -1))
…
}}}}}
Tensor IR
Space loop
Time loop
Restructure the loops
Specification

## Slide 22: Tiling
Array Partitioning
  Splitting an array into small partitions
  Partitions can be accessed in parallel
Annotation based on loop unrolling
%alloc = memref.alloc() {
partition_cyclic_array = [1],
partition_dim_array = [1],
partition_factor_array = [2]}
Matrix A
Partitioning dimension
cyclically
%alloc_0 = memref.alloc() {
partition_cyclic_array = [1],
partition_dim_array = [0],
partition_factor_array = [2]}
Matrix B
Partitioning dimension
cyclically
(0, 0)
(1, 0)
(0, 1)
(1, 1)
PE Array
Matrix A
2
1
3
2
1
3
Matrix B
SCF IR

## Slide 23: Vectorization
Enabling more parallelism
  Duplicating compute units in each PE
  Improve resource efficiency
Matrix A
2
1
3
(0, 0)
(1, 0)
(0, 1)
(1, 1)
PE Array
2
1
3
Matrix B
b0
a0

b1
a1


Vector Unit
X.vectorization(kk)
Specification
Restructure the loops
for (X.s0.i, 0, 8)
for (X.s0.j, 0, 8)
pipelined (X.s0.k, 0, 16)
unrolled (X.s0.ii, 0, 2)
unrolled (X.s0.jj, 0, 2)
unrolled (X.s0.kk, 0, 2)
…
Tensor IR

## Slide 24: Quick Try
Run:
./hls-tutorial run vanilla
./hls-tutorial run optimized
Then you will get:
 | Vanilla | Optimized
Cycle | 15411 | 2203
The optimized version achieves a 7X speedup compared to the vanilla version

## Slide 25: Synthesis Flow
Structural
Representation
Scheduling
Representation
ToR IR
HEC IR
Verilog
Hardware
IR
SCF IR
Tensor DSL
Tensor IR
GEMM, GEMV, DOT, GBMV, SYMV…
General Language
Software
IR
Control flow
Representation

## Slide 26: ToR IR
Provide a high-level control flow for hardware information
  Two parts, time graph and functional operations
tor.topo (0 to 7) {
tor.from 0 to 1 "seq:1"
tor.from 1 to 2 "seq:1"
tor.from 2 to 3 "call"
tor.from 1 to 4 "seq:2"
tor.from 3, 4 to 5 "if"
tor.from 5 to 6 "seq:1"
tor.from 0 to 7 "for"
}
0
1
2
4
3
5
6
7
1
1
2
@f
if
if
1
loop

## Slide 27: Time Graph
Four types of nodes including normal, call, if and loop
#cycles
sequential
call
@callee
sequential
sequential
if
if
sequential
back
loop
0
1
2
4
3
5
6
7
1
1
2
@f
if
if
1
loop

## Slide 28: Functional operations
Algorithmic specification with high-level information
  Bind each operation to the element of the time graph
tor.for %i = %c0 to %c10 step %c1 {
%m = tor.load %mask[%i] on (0 to 1)
%a = tor.if %m then {
%x = tor.addi %i %c1 on (1 to 2)
%y = tor.subi %i %c1 on (1 to 2)
%fx = tor.call @f(%x, %y) on (2 to 3)
tor.yield %fx
} else {
%ii = tor.muli %i %i on (1 to 4)
tor.yield %ii
} on (1 to 5)
tor.store %a to %A[%i] on (5 to 6)
} on (0 to 7)
0
1
2
4
3
5
6
7
1
1
2
@f
if
if
1
loop

## Slide 29: Functional operations
tor.for %i = %c0 to %c10 step %c1 {
%m = tor.load %mask[%i] on (0 to 1)
%a = tor.if %m then {
%x = tor.addi %i %c1 on (1 to 2)
%y = tor.subi %i %c1 on (1 to 2)
%fx = tor.call @f(%x, %y) on (2 to 3)
tor.yield %fx
} else {
%ii = tor.muli %i %i on (1 to 4)
tor.yield %ii
} on (1 to 5)
tor.store %a to %A[%i] on (5 to 6)
} on (0 to 7)
0
1
2
4
3
5
6
7
1
1
2
@f
if
if
1
loop
Algorithmic specification with high-level information
  Bind each operation to the element of the time graph

## Slide 30: Functional operations
tor.for %i = %c0 to %c10 step %c1 {
%m = tor.load %mask[%i] on (0 to 1)
%a = tor.if %m then {
%x = tor.addi %i %c1 on (1 to 2)
%y = tor.subi %i %c1 on (1 to 2)
%fx = tor.call @f(%x, %y) on (2 to 3)
tor.yield %fx
} else {
%ii = tor.muli %i %i on (1 to 4)
tor.yield %ii
} on (1 to 5)
tor.store %a to %A[%i] on (5 to 6)
} on (0 to 7)
0
1
2
4
3
5
6
7
1
1
2
@f
if
if
1
loop
Algorithmic specification with high-level information
  Bind each operation to the element of the time graph

## Slide 31: Supplementary information
Timing information like latency is attached to time graph
tor.topo (0 to 7) {
tor.from 0 to 1 "seq:1"
tor.from 1 to 2 "seq:1"
tor.from 2 to 3 "call"
tor.from 1 to 4 "seq:2"
tor.from 3, 4 to 5 "if"
tor.from 5 to 6 "seq:1"
tor.from 0 to 7 "for"
}

## Slide 32: Supplementary information
Timing information like latency is attached to time graph
Three scheduling manners are supported in ToR IR
  Static, pipeline and dynamic
tor.topo (0 to 7) {
tor.from 0 to 1 "seq:1"
tor.from 1 to 2 "seq:1"
tor.from 2 to 3 "call"
tor.from 1 to 4 "seq:2"
tor.from 3, 4 to 5 "if"
tor.from 5 to 6 "seq:1"
tor.from 0 to 7 "pipeline-for:1"
}
tor.for {...} on (0 to 7) {pipeline, II = 1}
0
1
2
4
3
5
6
7
1
1
2
@f
if
if
1
loop

## Slide 33: Supplementary information
loop
0
1
2
4
3
5
6
7
@f
if
if
Timing information like latency is attached to time graph
Three scheduling manners are supported in ToR IR
  Static, pipeline and dynamic
tor.topo (0 to 7) {
tor.from 0 to 1 "dynamic"
tor.from 1 to 2 "dynamic"
tor.from 2 to 3 "dynamic-call"
tor.from 1 to 4 "dynamic"
tor.from 3, 4 to 5 "dynamic-if"
tor.from 5 to 6 "dynamic"
tor.from 0 to 7 "dynamic-for"
}

## Slide 34: Quick Try
Then you will get several directories:
  examples/tor-raw/
  examples/tor-split/
  examples/hec/
  examples/chisel/
Run:
cd hector
cp $(which hector-opt) ./hector
bash examples/hls_script.sh hector examples

## Slide 35: SCF to TOR Compilation
cat examples/tor-raw/gemm_ncubed_kernel.mlir
tor.timegraph (0 to 15){
tor.succ 1 : [0 : i32] [{type = “static”}]
tor.succ 2 : [1 : i32] [{type = "static"}]
tor.succ 3 : [2 : i32] [{type = "static"}]
tor.succ 4 : [3 : i32] [{type = "static:1"}]
tor.succ 5 : [4 : i32] [{type = "static"}]
tor.succ 6 : [5 : i32] [{type = "static"}]
tor.succ 7 : [6 : i32] [{type = "static:1"}]
tor.succ 8 : [7 : i32] [{type = "static:1"}]
tor.succ 9 : [8 : i32] [{type = "static:9"}]
tor.succ 10 : [9 : i32] [{type = "static:13"}]
tor.succ 11 : [5 : i32] [{II = 14 : i32, pipeline = 1 : i32, type = "static-for"}]
tor.succ 12 : [11 : i32] [{type = "static"}]
tor.succ 13 : [12 : i32] [{type = "static:1"}]
tor.succ 14 : [2 : i32] [{type = "static-for"}]
tor.succ 15 : [1 : i32] [{type = "static-for"}]
}

## Slide 36: SCF to TOR Compilation
tor.for %arg0 = (%c0_i32 : i32) to (%c62_i32 : i32) step (%c1_i32 : i32)
on (1 to 14) {
tor.for %arg1 = (%c0_i32 : i32) to (%c62_i32 : i32) step (%c1_i32 : i32)
on (2 to 13) {
%3 = arith.shli %arg0, %c6_i32 {endtime = 4 : i32, starttime = 3 : i32} : i32
%4 = tor.for %arg2 = (%c0_i32 : i32) to (%c62_i32 : i32) step (%c1_i32 : i32)
on (5 to 10) iter_args(%arg3 = %cst) -> (f64) {
%6 = arith.shli %arg2, %c6_i32 {endtime = 7 : i32, starttime = 6 : i32} : i32
%7 = tor.addi %3 %arg2 on (6 to 7) : (i32, i32) -> i32
%8 = tor.load %0[%7] on (7 to 8) : !tor.memref<4096xf64, [], "r">[i32]
%9 = tor.addi %6 %arg1 on (6 to 7) : (i32, i32) -> i32
%10 = tor.load %1[%9] on (7 to 8) : !tor.memref<4096xf64, [], "r">[i32]
%11 = tor.mulf %8 %10 on (8 to 9) : f64
%12 = tor.addf %arg3 %11 on (9 to 10) : f64
tor.yield %12 : f64
} {II = 14 : i32, pipeline = 1 : i32}
%5 = tor.addi %3 %arg1 on (12 to 13) : (i32, i32) -> i32
tor.store %4 to %2[%5] on (12 to 13) : (f64, !tor.memref<4096xf64, [], "w">[i32])
}
}

## Slide 37: HEC IR
Adopt an allocate-assign mechanism
%m.lhs, rhs, res = primitive "mul_integer"
%sub.a, b, c = instance "sub" @mod
%i = wire "i"
hec.assign %m.lhs = %0
hec.assign %m.rhs = %1
//Case #1:
hec.assign %i = %m.res
//Case #2:
hec.assign %i = %2
res
*
lhs
rhs
c
mod
a
b
i
rhs=%1
lhs=%0
res
*
%2
Mux
i

## Slide 38: HEC IR
Three component styles corresponding to ToR
  State Transition Graph, Pipeline stages, Handshake
Start
Idle
Done
component @STG {
// allocations
stateset {
state @Idle {
// assigns
transition {
goto @Start if %cond
}
}
state @Start {
transition {
goto @Done
}
}
state @Done {
transition {
goto @Idle
}
}
}
} {style = "stg"}

## Slide 39: HEC IR
Three component styles corresponding to ToR
  State Transition Graph, Pipeline stages, Handshake
Start
Idle
Done
component @STG {
// allocations
stateset {
state @Idle {
// assigns
transition {
goto @Start if %cond
}
}
state @Start {
transition {
goto @Done
}
}
state @Done {
transition {
goto @Idle
}
}
}
} {style = "stg"}

## Slide 40: HEC IR
Three component styles corresponding to ToR
  State Transition Graph, Pipeline stages, Handshake
Stage 0
+
+
*
Stage 1
+
-
Stage 2
*
+
component @Pipe {
// allocations
stageset {
stage @stage0 {
// assigns
}
stage @stage1 {
// assigns
hec.assign %add2.lhs = %add0.res
hec.assign %add2.rhs = %add1.res
}
stage @stage2 {
// assigns
}
stage @stage3 {
// assigns
deliver %mul1.res, %add3.res
}
}
} {"pipeline",II=1}

## Slide 41: HEC IR
Three component styles corresponding to ToR
  State Transition Graph, Pipeline stages, Handshake
data
valid
ready
Handshake Protocol
Fork
Shift
Add
Merge
Latency-insensitive Design
component @Handshake (%in1,%in2,%out){
// allocations
%shift.in,res = primitive . "shift"
%add.lhs,rhs,res = primitive . "addi"
// elastic units
%merge.i1,i2,o = primitive . "merge"
%fork.i,o1,o2 = primitive . "fork"
graph {
assign %fork.i = %in1
assign %shift.in = %fork.o1
assign %add.lhs = %in2
assign %add.rhs = %f.o2
assign %merge.i1 = %shift.res
assign %merge.i2 = %add.res
assign %out = %merge.o
}
}{"handshake"}

## Slide 42: TOR to HEC Compilation
cat examples/hec/gemm_ncubed_kernel.mlir
hec.stage @s1{
%1 = hec.shift_left %r_5_i_1.reg %c6_i32 {dump = "comb_0"} : i32
hec.assign %r_8_2.reg = %1 : i32 -> i32
%2 = hec.addi %r_3_1.reg %r_5_i_1.reg {dump = "comb_1"} : (i32, i32) -> i32
hec.assign %r_9_2.reg = %2 : i32 -> i32
%3 = hec.addi %1 %r_4_1.reg {dump = "comb_2"} : (i32, i32) -> i32
hec.assign %r_10_2.reg = %3 : i32 -> i32
hec.assign %r_5_i_2.reg = %r_5_i_1.reg : i32 -> i32
hec.assign %r_6_2.reg = %r_6_1.reg : f64 -> f64
}
hec.stage @s2{
hec.assign %mem_global_0.addr = %r_9_2.reg : i32 -> i12
hec.enable %mem_global_0.r_en : i1
hec.assign %mem_global_1.addr = %r_10_2.reg : i32 -> i12
hec.enable %mem_global_1.r_en : i1
hec.assign %r_5_i_3.reg = %r_5_i_2.reg : i32 -> i32
hec.assign %r_6_3.reg = %r_6_2.reg : f64 -> f64
hec.assign %r_9_3.reg = %r_9_2.reg : i32 -> i32
hec.assign %r_10_3.reg = %r_10_2.reg : i32 -> i32
}

## Slide 43: TOR to HEC Compilation
cat examples/hec/gemm_ncubed_kernel.mlir
hec.component @outline_0(%arg0: i32,%arg1: i32,%arg2: i32,%arg3: i32,%arg4: i32,%arg5: i1) -> (%arg6: f64,%arg7: i1)
{interface="naked", style="pipeline"}{
%r_13_13.reg = hec.primitive "r_13_13" is "register" : f64
%mulf_outline_0_0.operand0, operand1, result = hec.primitive
"mulf_outline_0_0" is "mul_float" : f64, f64, f64
}
hec.component @main(%arg0: i1) -> (%arg1: i1)
{interface="naked", style="STG"}{
%r_main_0.reg = hec.primitive “r_main_0” is “register” : i1
%r_main_1.reg = hec.primitive "r_main_1" is "register" : i1
%r_main_2.reg = hec.primitive "r_main_2" is "register" : i32
%r_main_3.reg = hec.primitive "r_main_3" is "register" : i32
%outline_0_0.in0, in1, in2, in3, in4, go, out0, done = hec.instance
"outline_0_0" @outline_0 : i32, i32, i32, i32, i32, i1, f64, i1
}

## Slide 44: RTL Generation
cat examples/chisel/gemm_ncubed_kernel.scala
class main extends MultiIOModule {
val done = IO(Output(Bool()))
done := 0.U
val outline_0_0 = Module(new outline_0)
val var8 = IO(Output(UInt(64.W)))
object State extends ChiselEnum { val s0, s1, s1_entry, s2, s2_entry, s3, s4, s5, s5_wait, s6, s7, s8, s9, s10 = Value }
val state = RegInit(State.s0)
switch (state) {
is (State.s1) {
val var90 = 0.U <= 62.U
var76 := var90
val var91 = !var90
state := State.s2;
when (var91.asBool()) { state := State.s10; }
}
is (State.s10) { done := 1.U }
}
}

## Slide 45: Hestia
An efficient cross-level debugger for HLS designs that enables breakpoints and stepping at multiple granularity
Debug
Interface
software
level
schedule
level
structure
level
Multi-level
Interpreter
sync
sync
Equivalence
Mapping
SCF
TOR
HEC
IR
generate
exec
verify
cmd
check
cmd
check
cmd
check
Breakpoint
Watchpoint
Step
Continue
Switch
Load
……

## Slide 46: Debugging at SCF
cd hestia
hestia
exit

## Slide 47: Debugging at SCF
cd tutorial/examples/case1
hestia command.tcl
continue
mem op_3
exit
cat data/D_out.txt
load scf.json
load_memory_file op_0 data/A.txt
load_memory_file op_1 data/B.txt
load_memory_file op_2 data/C.txt
call main
RETURN:
op_3 Memory {
store: [
I32(30773412), I32(43773702), I32(39399768), I32(42375816),
I32(39878346), I32(46819968), I32(38864916), I32(42650712),
I32(41010798), I32(41823036), I32(32292810), I32(33290802),
I32(41601426), I32(40812594), I32(42230898), I32(43038654),
I32(32263200), I32(44749656), I32(40505076), …
]
}
Differs from output result.

## Slide 48: Debugging interface
hestia command.tcl
breakpoint op_116
continue
var op_115
unset_breakpoint op_116
show_breakpoint
watch op_135_b
watch op_131_b
watch op_115
step 10000
show_op
step 2
SHOW VALUE:
op_115 I32(0)
SHOW VALUE:
op_115 I32(6)
op_135_b I32(1)
op_131_b I32(3)
op_115 I32(6)
op_135_b I32(1)
op_131_b I32(3)
op_115 I32(6) …
Computation { operands: ["op_135_b", "op_113"], op_type: "shift_left", name: "op_114", ret_type: "i32" }
SHOW VALUE:
op_115 I32(6)
op_135_b I32(1)
op_131_b I32(3)
op_115 I32(7)
op_135_b I32(1)
op_131_b I32(3)

## Slide 49: Multi-level Interpreter
Schedule simulation is organized as an instance pool
  valuable insights into the timing behavior of the design
Instance pooling
Function list
Top (stall)
s1
s2
s3
Top:
Dataflow
s1, s2, s3
…
Son:
Pipeline II=3
Time Graph
Operation
…

## Slide 50: Multi-level Interpreter
Schedule simulation is organized as an instance pool
  valuable insights into the timing behavior of the design
Instance pooling
Function list
Top (stall)
s1
s2
s3
Pipeline
Env
Env
Env
Env
op_56:
I32(336)
op_67:
F32(2.11234)
…
Stage list
[1, 4, 7]
Top:
Dataflow
s1, s2, s3
…
Son:
Pipeline II=3
Time Graph
Operation
…

## Slide 51: Multi-level Interpreter
Structural interpreter constructs a hierarchical structure
  Controller, primitives, sub-modules
Top
Primitives
Modules
Controller
State Transition Graph
S2
S0
S1
Assignments
assign %f1.in=%a
assign %Add.in=%b
…
S3
Primitives
Instances
StageSet
S2
Primitives
Instances
StageSet
S1
Primitives
Modules
Controller
…

## Slide 52: Multi-level Interpreter
Structural interpreter constructs a hierarchical structure
  Controller, primitives, sub-modules
Top
Primitives
Modules
Controller
State Transition Graph
S2
S0
S1
Assignments
assign %f1.in=%a
assign %Add.in=%b
…
S3
Primitives
Instances
StageSet
S2
Primitives
Instances
StageSet
S1
Primitives
Modules
Controller
…
Propagate & update
Mul_7
operand0 = I32(23)
operand1 = I32(31)
result = I32(713)
Reg_2
operand0 = I32(27)
Add_1
operand0 = I32(23)
operand1 = I32(131)
result = I32(154)
Multiplier
Register
Adder
Ports
Inner
state
…

## Slide 53: Simulation Speedup
cd ../../benchmarks/collection1
time hestia command/aeloss_push/tor.tcl
time hestia command/aeloss_push/hec.tcl
 | TOR IR | HEC IR
Cycle | 1502609 | 1502706
Time | 2.019s | 37.711s

## Slide 54: Debugging at TOR & HEC levels
cd ../../examples/case2
hestia tor.tcl
cat data/C_out.txt
load tor.json
load_memory_file op_0 data/C.txt
load_memory_file op_1 data/A.txt
load_memory_file op_2 data/B.txt
call main
continue
mem op_0
exit
Cycle count: 26283
op_0 Memory{
store: [
I32(738698), I32(34), I32(90), I32(26), I32(24), I32(57),
I32(14), I32(68), I32(5), I32(58), I32(12), I32(86), I32(0),
I32(46), I32(26), I32(94), I32(1099936), I32(1070152),
I32(78), I32(29), I32(46), I32(90), I32(47), I32(70), I32(51),
I32(80), I32(31), I32(93), I32(57), I32(27), I32(12), …
]
}
Same as the output result.

## Slide 55: Debugging at TOR & HEC levels
hestia hec_wrong.tcl
load hec_wrong.json
load_memory_file mem_global_0 data/C.txt
load_memory_file mem_global_1 data/A.txt
load_memory_file mem_global_2 data/B.txt
call main
continue
mem mem_global_0
exit
thread 'main' panicked at src/lib/basetype.rs:168:35:
index out of bounds: the len is 256 but the index is 256

## Slide 56: Debugging at TOR & HEC levels
hestia cosim.tcl
load tor.json
load_memory_file op_0 data/C.txt
load_memory_file op_1 data/A.txt
load_memory_file op_2 data/B.txt
call main
load hec_wrong.json
#load hec.json
load_memory_file mem_global_0 data/C.txt
load_memory_file mem_global_1 data/A.txt
load_memory_file mem_global_2 data/B.txt
call main
load_equal equal.json
cosim
exit
thread 'main' panicked at src/lib/equal.rs:77:17:
assertion `left == right` failed:
Value Mismatch:
operation "op_44" and primitive "muli_main_0”
at state @s14
left: I32(624)
right: I32(432)

## Slide 57: Debugging at TOR & HEC levels
hestia cosim.tcl
diff hec_wrong.json hec.json
load tor.json
load_memory_file op_0 data/C.txt
load_memory_file op_1 data/A.txt
load_memory_file op_2 data/B.txt
call main
#load hec_wrong.json
load hec.json
load_memory_file mem_global_0 data/C.txt
load_memory_file mem_global_1 data/A.txt
load_memory_file mem_global_2 data/B.txt
call main
load_equal equal.json
cosim
exit
Cosimulation Pass

## Slide 58: Summary
Multi-level IR infrastructure
  Shows remarkable flexibility to domain-specific applications
Systolic array generation
  Achieves optimization in specific tasks through sophisticated dataflow and loop transformations, enhancing performance.
High-level synthesis and debugger
  Essential for reliable hardware design and verification

## Slide 59: RTL Simulator with Cross-Cycle Optimization
Speaker: Kexing Zhou
周可行

## Slide 60: Khronos: RTL Simulator with Cross-Cycle Optimization
Cement
(cmt2)
Hector
Chisel
Test
bench
Verilog
(yosys)
Khronos
(ksim)
Frontend Languages
Khronos Inputs
EXE File
(sim.exe)
Origen
Covered in This Section
Covered in CMT/Origen
Cross-cycle optimization

## Slide 61: Outline
Compilation workflow of Khronos
  Input Preparation
  Header and Code Generation
  Testbench Preparation
  Compile and Linking
Intermediate Representation of Khronos
  Flattening, Fusing, Lowering, Queuing
Real Application Evaluation

## Slide 62: Outline
Compilation workflow of Khronos
  Input Preparation
  Header and Code Generation
  Testbench Preparation
  Compile and Linking
Intermediate Representation of Khronos
  Flattening, Fusing, Lowering, Queuing
Real Application Evaluation

## Slide 63: Compilation Flow of Khronos
(1) firtool-ksim --ir-hw $1.fir -o $1.mlir
(2) ksim $1.mlir -v -o $1.ll --out-header=$1.h
(3) llc-ksim -O2 -filetype=obj $1.ll -o $1.o
(4) clang++ -O2 $1.o $1.cpp -o $1
firtool
Khronos
(ksim)
cpp
(.h)
LLVM
(.ll)
CIRCT
(.mlir)
Compile & Link
sim
(.exe)
Test
bench
(1) .fir -> .mlir
(2) run ksim
(3) .ll -> .o
(4) .cpp, .o -> .exe
Khronos is based on MLIR & CIRCT
firtool: Translate input to CIRCT IR
ksim:
  Translate hw logic to llvmir
  Generate header file for testbench
llc: compile llvmir to linkable object
clang++: compile and link testbench
Command Cheet Sheet

## Slide 64: Khronos Flow: Prepare Input
circuit SimpleFIR:
module SimpleFIR:
input clock: Clock
input reset: UInt<1>
input in: SInt<16>
output sum: SInt<16>
reg r1: SInt<16>, clock
reg r2: SInt<16>, clock
reg r3: SInt<16>, clock
r1 <= in
r2 <= r1
r3 <= r2
sum <= add(add(in, r1), add(r2, r3))
module {
......
hw.module @SimpleFIR( %clock: i1,
%reset: i1, %in: i16) -> (sum: i16) {
%r1 = seq.firreg %in clock %clock {...} : i16
%r2 = seq.firreg %r1 clock %clock {...} : i16
%r3 = seq.firreg %r2 clock %clock {...} : i16
%0 = comb.add %in, %r1, %r2, %r3 : i16
hw.output %0 : i16
}
}
firtool-ksim simplefir.fir -ir-hw \
-o simplefir.mlir
Please enter `ksim/example` and open `simplefir.fir`.
Top modules names the same as circuit
Basic type, `UInt` and `SInt`
Use `<=` to connect signals
Translate it to CIRCT IR
module => `hw.module`
comb logics => `comb.xxx`
registers => `seq.firreg`
simplefir.fir
simplefir.mlir
This is a FIRRTL file.

## Slide 65: Khronos Flow: Generate Header and IR
ksim simplefir.mlir \
--out-header=simplefir.h \
-o simplefir.ll
#pragma once
...
__attribute__((weak)) /* input */ uint8_t reset; // i1
__attribute__((weak)) /* input */ uint16_t in; // i16
__attribute__((weak)) /* output */ uint16_t sum; // i16
void SimpleFIR();
#define eval SimpleFIR
#define SimpleFIR_output_ahead 0
#define SimpleFIR_reset_ahead 0
...
define void @SimpleFIR() {
%1 = load i16, ptr @in, align 2
%2 = load i16, ptr @in_0, align 2
store i16 %1, ptr @in_0, align 2
%3 = load i16, ptr @queue, align 2
store i16 %2, ptr @queue, align 2
%4 = load i16, ptr @queue_0, align 2
store i16 %3, ptr @queue_0, align 2
%5 = add i16 %1, %2
%6 = add i16 %5, %3
%7 = add i16 %6, %4
store i16 %7, ptr @sum, align 2
ret void
}
module {
......
hw.module @SimpleFIR( %clock: i1,
%reset: i1, %in: i16) -> (sum: i16) {
%r1 = seq.firreg %in clock %clock {...} : i16
%r2 = seq.firreg %r1 clock %clock {...} : i16
%r3 = seq.firreg %r2 clock %clock {...} : i16
%0 = comb.add %in, %r1, %r2, %r3 : i16
hw.output %0 : i16
}
}
simplefir.mlir
simplefir.ll
Compile the file using Khronos
simplefir.h
.ll file contains the logic of simulator
.h file contains IO signals
`clock` is removed in IO signals
call the eval function to advance 1 cycle

## Slide 66: Khronos Flow: Prepare Testbench
ksim simplefir.mlir \
--out-driver=simplefir.cpp \
-o simplefir.ll
int main(int argc, char ** argv) {
int cnt = atoi(argv[1]);
reset = 1;
for(auto i = SimpleFIR_reset_ahead; i >= 0; i--) {
SimpleFIR();
reset = 0;
}
auto start = system_clock::now();
for(auto i = 0; i < cnt; i++) {
SimpleFIR();
}
auto stop = system_clock::now();
// ...
return 0;
}
simplefir.cpp
int main(int argc, char ** argv) {
int cnt = atoi(argv[1]);
reset = 1;
for(auto i = SimpleFIR_reset_ahead; i >= 0; i--) {
SimpleFIR();
reset = 0;
}
auto start = system_clock::now();
for(auto i = 0; i < cnt; i++) {
in = i;
SimpleFIR();
printf(“cycle=%d in=%d sum=%d\n”, i, in, sum);
}
auto stop = system_clock::now();
// ...
return 0;
}
simplefir.cpp
Khronos can generate a skeleton testbench
Add custom peek/poke statements in the testbench
Set in port `in` to the cycle number
Print the IO signal of the circuit

## Slide 67: Khronos Flow: Compile, Link and Run
./simplefir 10
❯ ./simplefir 10
cycle=0 in=0 sum=0
cycle=1 in=1 sum=1
cycle=2 in=2 sum=3
cycle=3 in=3 sum=6
cycle=4 in=4 sum=10
cycle=5 in=5 sum=14
cycle=6 in=6 sum=18
cycle=7 in=7 sum=22
cycle=8 in=8 sum=26
cycle=9 in=9 sum=30
112
Use llc (llvmir compiler) to compile the generated code
llc-ksim --filetype=obj \
simplefir.ll -o simplefir.o
Use clang++ to compile testbench and link exe file
clang++ simplefir.cpp simplefir.o -o simplefir
Run the simulator
(This is elapsed time)

## Slide 68: Outline
Compilation workflow of Khronos
  Input Preparation
  Header and Code Generation
  Testbench Preparation
  Compile and Linking
Intermediate Representations in Khronos
  Flattening, Fusing, Lowering, Queuing
Real Application Evaluation

## Slide 69: Intermediate Representation of Khronos
Khronos has many internal IR
  flattened: flatten modules to build graph
  fused: fuse registers
  low: register => queue
--out=<value> - Output file type
=core - Default circt core IR
=flattened - Ksim high level ir
=fused - Ksim fused ir
=low - KSim low level ir
=llvm - LLVM dialect
=llvmir - LLVM IR
ksim --help
(1) flatten
(2) fuse
(3) lower

## Slide 70: Phase 1: Flatten
circuit Tree:
module Tree:
input clock: Clock
input reset: UInt<1>
input in: SInt<16>[4]
output sum: SInt<16>
reg r0: SInt<16>, clock
reg r1: SInt<16>, clock
reg r2: SInt<16>, clock
r0 <= add(in[0], in[1])
r1 <= add(in[2], in[3])
r2 <= add(r0, r1)
sum <= r2
tree.fir
module {
hw.module @Tree(%clock: i1, %reset: i1,
%in_0: i16, %in_1: i16,
%in_2: i16, %in_3: i16) -> (sum: i16) {
%r0 = seq.firreg %0 clock %clock {...} : i16
%r1 = seq.firreg %1 clock %clock {...} : i16
%r2 = seq.firreg %2 clock %clock {...} : i16
%0 = comb.add %in_0, %in_1 : i16
%1 = comb.add %in_2, %in_3 : i16
%2 = comb.add %r0, %r1 : i16
hw.output %r2 : i16
}
}
tree.flattened.mlir
Please enter `ksim/example` and open `tree.fir`
Translate it to mlir
firtool-ksim tree.fir -ir-hw -o tree.mlir
Show ksim IR:
ksim tree.mlir -out=flattened -o tree.flattened.mlir
Only one module,
flattened IR is identical to mlir

## Slide 71: Phase 2: Fusing
module {
hw.module @Tree(%clock: i1, %reset: i1,
%in_0: i16, %in_1: i16,
%in_2: i16, %in_3: i16) -> (sum: i16) attributes {
ksim.output_ahead = 2 : i64
} {
%r0 = seq.firreg %0 clock %clock {ksim.delay=0:i64} : i16
%r1 = seq.firreg %1 clock %clock {ksim.delay=0:i64} : i16
%r2 = seq.firreg %2 clock %clock {ksim.delay=0:i64} : i16
%0 = comb.add %in_0, %in_1 : i16
%1 = comb.add %in_2, %in_3 : i16
%2 = comb.add %r0, %r1 : i16
hw.output %r2 : i16
}
}
ksim.fused.mlir
module {
hw.module @Tree(%clock: i1, %reset: i1,
%in_0: i16, %in_1: i16,
%in_2: i16, %in_3: i16) -> (sum: i16) {
%r0 = seq.firreg %0 clock %clock {...} : i16
%r1 = seq.firreg %1 clock %clock {...} : i16
%r2 = seq.firreg %2 clock %clock {...} : i16
%0 = comb.add %in_0, %in_1 : i16
%1 = comb.add %in_2, %in_3 : i16
%2 = comb.add %r0, %r1 : i16
hw.output %r2 : i16
}
}
tree.flattened.mlir
Run state fusion algorithm in Khronos
ksim tree.flattened.mlir \
-in=flattened -out=fused \
-o tree.fused.mlir
After state fusion
“ksim.delay” attribute is attached to each register
if delay = 0, it is fused, and will be remove later
“output_ahead” captures how many cycles output advanced

## Slide 72: Phase 3: Lowering
module {
ksim.low.def_queue @clock depth 1 : i1 delay [0]
ksim.low.def_queue @reset depth 1 : i1 delay [0]
ksim.low.def_queue @in_0 depth 1 : i16 delay [0]
ksim.low.def_queue @in_1 depth 1 : i16 delay [0]
ksim.low.def_queue @in_2 depth 1 : i16 delay [0]
ksim.low.def_queue @in_3 depth 1 : i16 delay [0]
ksim.low.def_queue @sum depth 1 : i16 delay [0]
func.func @Tree() attributes {ksim.output_ahead = 2 : i64} {
%0 = ksim.low.get_queue @in_0[0] : i16
%1 = ksim.low.get_queue @in_1[0] : i16
%2 = ksim.low.get_queue @in_2[0] : i16
%3 = ksim.low.get_queue @in_3[0] : i16
%4 = comb.add %0, %1, %2, %3 : i16
ksim.low.push_queue @sum %4 : i16
return
}
}
tree.low.mlir
ksim tree.fused.mlir \
-in=fused -out=low \
-o tree.low.mlir
Lower the fused IR to low level queue IR
IO, registers are converted to queue
Register R/W ops are converted to `get_queue`, `push_queue` ops

## Slide 73: Outline
Compilation workflow of Khronos
  Input Preparation
  Header and Code Generation
  Testbench Preparation
  Compile and Linking
Intermediate Representation of Khronos
  Flattening, Fusing, Lowering, Queuing
Real Application Evaluation

## Slide 74: Real Application Evaluation
We run khronos on real world design, Gemmini
  A full run is time consuming, we only run khronos on its core PE array
  Please enter `ksim/example`
firtool-ksim Mesh6x6.fir --ir-hw -o Mesh6x6.mlir
ksim Mesh6x6.mlir \
--out-header=Mesh6x6.h \
--out-driver=Mesh6x6.cpp \
-o Mesh6x6.ll
llc-ksim -O2 \
--relocation-model=dynamic-no-pic \
--filetype=obj \
Mesh6x6.ll -o Mesh6x6.ksim.o
clang++ -O2 Mesh6x6.cpp Mesh6x6.ksim.o -o Mesh6x6
firtool-ksim Mesh6x6.fir -o Mesh6x6.v
verilator --cc --exe --build \
Mesh6x6.v Mesh6x6.tb.cpp
Compile it using khronos
Compile it using verilator
The compilation is a little slow

## Slide 75: Real Application Evaluation
The testbench will print elapsed time, run each tb and compare the result
Result varies on your platform
❯ ./obj_dir/VMesh6x6 100000
1759708
❯ ./Mesh6x6 100000
200646
Khronos
Verilator
8.77x faster

## Slide 76: HDL and Framework for Chip Design
Speaker: Youwei Xiao, Zizhang Luo
肖有为 罗梓璋

## Slide 77: Cement: Better HDL and Framework for Chip Design
Traditional HDL
tedious hardware code
Embedded HDL (eHDL)
design hardware in advanced programming language (Scala, Python)
HLS: design hardware in C/C++
Cement (cmt1)
published at FPGA’24
Youwei Xiao, Zizhang Luo, Kexing Zhou, and Yun Liang. 2024. Cement: Streamlining FPGA Hardware Design with Cycle-Deterministic eHDL and Synthesis. FPGA '24. https://doi.org/10.1145/3626202.3637561
software-like control description
High-level HDL: describe hardware as rules
Cement (cmt2!)
keep evolving…
Rust-embedded HDL
rule-based design
?

## Slide 78: Today, we introduce cmt2!
software-like control description
Rust-embedded HDL
rule-based design
as the successor of …
Cement (cmt1)
published at FPGA’24
cmt2!

## Slide 79: We choose Rust, because…
Rust has been the top admired programming language for 7 consecutive years
In our own experience, it’s powerful, efficient, user-friendly
Rust is admired by 82.2%!

## Slide 80: In Rust, cmt2 project looks like…
include necessary build flags
Here, 5 library crates forms the cmt2 package
cmtrs eHDL
cmtir IR
kir
backends
cmtc
compiler
specify rust version
specify package information and dependencies
cd $REPOS/cmt2 && ls –a

## Slide 81: Hello Rust World!
click [run] above fn main, or …
Cargo is Rust’s build system and package manager. It’s easy-to-use!
More user-friendly than sbt for Scala/Chisel!
create hello.rs file ↑
touch $REPOS/cmt2/crates/cmtc/examples/hello.rs
cargo run --example hello
under directory $REPOS/cmts

## Slide 82: Hello cmt2!
at the top of hello.rs
use clauses import cmt2’s eHDL and compiler features
itfc_declare! is a macro
macro in Rust transforms code at the token-level
If curious, feel free to run (if have internet connection):
to see the transformed code!
cargo install cargo-expand
cd $REPOS/cmt2/crates/cmtc
cargo expand --example hello

## Slide 83: Hello cmt2!
macro is an advanced feature in Rust!
Please leave cmt2 developers to suffer😂
and… just use them!😁
The left code creates …
A module interface named A2B;
It has one input port a, one output port b, both of which have type T.
It exposes a method run for external world to invoke!
a:T
b:T
method run
A2B
at the top of hello.rs

## Slide 84: cmt2 is rule-based HDL
a:T
b:T
method run
Hardware logic is organized as rules – the execution unit!
Don’t be afriad!😁
Just consider one rule as a group of operations that execute together
In cmt2, we have two types of rules: method rules and always rules:
method rule need to be invoked (Bluespec method)
always rule runs actively (Bluespec rule)
A2B
at the top of hello.rs
rule-based design
cmt2!

## Slide 85: cmt2 is rule-based HDL
following itfc_declare!
fn starts a function!
The #[module] macro transfoms the function add1 to create a module of the interface A2B
a:T
b:T
method run
A2B
add1 of
UInt(4)
b=a+1
Now, types are given, rules are filled -- Module is completely described!

## Slide 86: cmt2 generates SystemVerilog
following fn add1
The new main function to call elaborate for the add1 module
click [run] above fn main, or …
cargo run --example hello
cat add1.sv

## Slide 87: Show features by examples
software-like control description
Rust-embedded HDL
rule-based design
as the successor of …
Cement (cmt1)
published at FPGA’24
cmt2!
FIR
GEMM

## Slide 88: Finite Impulse Response
Type Parameter
Name of Interface/Module
An input port
named “in_”
of type T
rename
A method to input data
A method to output data
./crates/cmtc/examples/fir.rs line 7-16
Rust-embedded HDL
cmt2!

## Slide 89: FIR Example1: fixed length
Parameters: type & coefficients
Return a module with interface type FIR
io! macro provides parameters and gets an io struct
instantiate a
Reg as submodule
implement a method
called “input”
input of the method
things to do after the method is invoked
reg %= xx is a syntax sugar for reg.write(xx)
./crates/cmtc/examples/fir.rs line 18-46
rule-based design

## Slide 90: FIR Example1: fixed length
implement an always rule called “shift”
shift the registers
implement the output method
return an expression
calculate FIR
convert software value a2 into hardware literal of type t
./crates/cmtc/examples/fir.rs line 18-46

## Slide 91: FIR Example2: arbitrary length
An array of coefficients
Still returns FIR
Instantiate
a vector of
Regs
Input to the first reg
./crates/cmtc/examples/fir.rs line 48-78
Rust-embedded HDL

## Slide 92: FIR Example2: arbitrary length
Generate n-1 shifts with a software for expression
Make a multiply accumulate expression with functional programming
./crates/cmtc/examples/fir.rs line 48-78

## Slide 93: Explanation on the last expression
reg0
reg1
reg2
reg3
regs
a0
a1
a2
a3
a
iter()
zip()
For audiences that are not familiar with functional programming
map()
reduce()
Option<Sum>
Sum
unwrap()
Rust-embedded HDL

## Slide 94: FIR Example3: adder tree
collect multiply results
generate an adder tree
a gen_fn generates hardware
Variables that will be added
The returned sum
generate one pipeline reg
generate one pipeline reg
for the sum
recursive to calculate the left part and the right part
generate one pipeline reg
for the sum
./crates/cmtc/examples/fir.rs line 83-123

## Slide 95: FIR Example: Testbench preparation
the interface for the testbench
pass the DUT into the TB
tell the compiler this is a TB
instantiate DUT
a cycle counter for simulation
a rust random generator
./crates/cmtc/examples/fir.rs line 132-174

## Slide 96: FIR Example: Testbench inputs
make 10 inputs
make 10 always rules with different name
rule guard
generate an input,
call method
print the input
./crates/cmtc/examples/fir.rs line 132-174

## Slide 97: FIR Example: Testbench inputs
rule guard
print during simulation
call method
finish simulation at cycle 20
increase cycle counter
./crates/cmtc/examples/fir.rs line 132-174

## Slide 98: FIR Example: Elaboration & Simulation
cd $REPOS/cmt2
cargo run –-example fir
cd ./tb/fir_tb1_ksim
make all
./FIR_s6
main function of Rust
Type: 16-bit signed int
Generate a FIR (first example)
Elaborate to generate SV
Generate a TB
(FIR is regenerated here)
Elaborate to generate Khronos simulation environment
run Rust
run Khronos
run the simulation program
Possible Outputs
./crates/cmtc/examples/fir.rs line 176-204

## Slide 99: General Matrix Multiplication
A Mem
B Mem
C Mem
MAC
F
S
M
data type
address type
memory as nested interface
GEMM
write()
read()
simple methods to start computation and report finish
./crates/cmtc/examples/gemm.rs line 25-36
software-like control description
cmt2!

## Slide 100: GeMM Example: Software
GeMM in C using three for-loops
C
A
B
k
k
i
j

## Slide 101: GeMM Example: Preperation
calculate the address type
provide the memory instances to the interface
some register for loops
one MAC unit
one accumulator
./crates/cmtc/examples/gemm.rs line 38-97

## Slide 102: GeMM Example: FSM
keyword
a for loop
init: i=0
i<n i=0 => 0<n
update: i=i+1
i<n i=i+1 => i<n-1
i= 0 to n-1
j= 0 to n-1
./crates/cmtc/examples/gemm.rs line 38-97
software-like control description

## Slide 103: GeMM Example: FSM innermost body
for i in 0..n
  for j in 0..n
the following steps will be done in a sequence
generate n steps
feed memory address
get memory data
invoke MAC
accumulate result
amem.rd0
bmem.rd1
amem.rd1
bmem.rd1
mac
acc
Seq
step0
step1
step2
step3
amem.rd0
bmem.rd1
amem.rd1
bmem.rd1
mac
acc
amem.rd0
bmem.rd1
amem.rd1
bmem.rd1
mac
acc
amem.rd0
bmem.rd1
The same for all n steps
./crates/cmtc/examples/gemm.rs line 38-97

## Slide 104: GeMM Example: FSM last step
for i in 0..n
  for j in 0..n
Seq
step0
step1
step2
step3
amem.rd0
bmem.rd1
amem.rd1
bmem.rd1
mac
acc
amem.rd0
bmem.rd1
amem.rd1
bmem.rd1
mac
acc
amem.rd0
bmem.rd1
amem.rd1
bmem.rd1
mac
acc
amem.rd0
bmem.rd1
step n
amem.rd1
bmem.rd1
mac
acc
cmem.write
last mem read and MAC
write to cmem
./crates/cmtc/examples/gemm.rs line 38-97

## Slide 105: GeMM Example: Simulation
Expected results
Cycles= ( //k
//j
//i
= 4369
4370
+ 1 cycle to write finish
+ 1 cycle to init
+ 1 cycle to init
Commands to run simulation
cd $REPOS/cmt2
cargo run –-example gemm
cd ./tb/gemm_ksim
make all
./GEMM_s16_i8

## Slide 106: GeMM unrolled Example: Interface Declare
Mem
Mem
C Mem
GEMM
Unrolled
MAC
MAC
MAC
MAC
Mem
Mem
Mem
Mem
Mem
Mem
FSM
Multi-bank 2D memory
./crates/cmtc/examples/gemm_unrolled.rs line 25-36

## Slide 107: GeMM unrolled Example: unroll factor
A
B
C
Iter 1
unroll factor=4
Iter 2
Iter 3
Iter 4

## Slide 108: GeMM unrolled Example
i
j
k
./crates/cmtc/examples/gemm_unrolled.rs
line 38-114

## Slide 109: GeMM unrolled Example: innermost
Each inner loop have n/factor+1 steps
for i in 0..n
  for j in 0..n
read factor memory banks at the same time
invoke factor MACs and accumulate
get the sum of all accumulators
write to c memory
./crates/cmtc/examples/gemm_unrolled.rs
line 38-114

## Slide 110: GeMM unrolled Example: Simulation
1298
Commands to run simulation
Factor=4 results
Cycles= ( //k
//j
//i
= 1297
4370/12983.37
cd $REPOS/cmt2
cargo run –-example gemm_unrolled
cd ./tb/gemm_unrolled_ksim
make all
./GEMMUnrolled_s16_i8

## Slide 111: use cmt2 as a library
When you’re building a rust project…
Add rust version and build flag
Add cmt2 from crates.io!
This need internet!
Now, feel free to use cmt2 for hardware design
cd $REPOS && cargo new hello
cp -r ./cmt2/.cargo ./cmt2/rust-toolchain.toml ./hello
cd hello
cargo add cmtrs cmtc anyhow
cp ../cmt2/crates/cmtc/examples/hello.rs ./src/main.rs && cargo run

## Slide 112: use cmt2 as a library
When you’re building a rust project…
Add rust version and build flag
Add cmt2 from crates.io!
This need internet!
Now, feel free to use cmt2 for hardware design
cd $REPOS && cargo new hello
cp -r ./cmt2/.cargo ./cmt2/rust-toolchain.toml ./hello
cd hello
cargo add cmtrs cmtc anyhow
cp ../cmt2/crates/cmtc/examples/hello.rs ./src/main.rs && cargo run

## Slide 113: LLM-Based Chip Design
Speaker: Fan Cui
崔璠

## Slide 114: Outline
Introduction
  LLM-Driven Hardware Design
Warmup
  Adder
GEMM
  Testbench
  Kernel

## Slide 115: OriGen Model
Using the two datasets obtained in code-to-code augmentation
We train OriGen model based on Qwen-Coder

## Slide 116: Complex Hardware Design Flow
For complex hardware, it is hard for LLM to implement the module fully autonomously.
The flow is step-by-step and needs human guidance, especially in the debug process.

## Slide 117: Complex Hardware Design Flow
The initial prompt is critical, establishing the module's foundational behavior, adequate guidance from human is helpful.
LLMs can generate both testbench and kernel, but the testbench needs to be validated by human.

## Slide 118: Complex Hardware Design Flow
In the design flow, the LLM first generates the testbench based on the specification and then uses it to validate the kernel.
If the testbench or kernel contains bugs, minor syntax errors can be automatically corrected based on compiler feedback.
Complex logic bugs need human guidance

## Slide 119: Complex Hardware Design Flow
If we need to design several kernels, the previous design can serve as a reference to speed up the process.

## Slide 120: Outline
Introduction
  LLM-Driven FPGA Kernel Design
Warmup
  Adder
GEMM
  Testbench
  Kernel

## Slide 121: Chat Interface
The chat interface is on origen.ahs.ericlyun.me
Please sign up first
Then you will see the chat interface

## Slide 122: Prompts
To ensure consistent chat behavior, we've saved the prompts in the prompt directory.
You can access it on https://github.com/pku-liang/origen_examples
Each numbered file contains the prompts for the corresponding conversation round.

## Slide 123: Warmup
First, we ask LLM to generate a simple 8 bit adder and simulate using ksim.
Copy the prompt of 1.txt

## Slide 124: Warmup
The generated code is too complicated!
Copy the prompt of 2.txt to simplify.
Much better now

## Slide 125: Warmup
Now run run.sh under adder to simulate in ksim
The result is as expected
bash $REPOS/origen/adder/run.sh

## Slide 126: Outline
Introduction
  LLM-Driven FPGA Kernel Design
Warmup
  Adder
GEMM
  Testbench
  Kernel

## Slide 127: GEMM
In this case, we will use OriGen to generate both the testbench and kernel for GEMM.
We use single-cycle latency multiplier
Dual port ram
  Initialized from a hex file
  Synchronous write
  Asynchronous read
Defined in utils/lib.sv

## Slide 128: Code
The testbench and kernel code is approximately 100 lines long, so it may take LLM some time to generate.
We have saved the generated code of each round under code directory
You can access it on https://github.com/pku-liang/origen_examples
We will generate the testbench first, followed by the kernel.

## Slide 129: Testbench
Copy the prompt in 1.txt
Module Configuration, Key Interfaces and Test Storage in the prompt

## Slide 130: Testbench
Copy the LLM’s output to gemm_tb.sv
The result seems nice, but there is a syntax error
Let's see if the LLM can fix it.
(Copy the prompt in 2.txt)
touch $REPOS/origen/gemm/testbench/gemm_tb.sv

## Slide 131: Testbench
Use iverilog to test again, we can find the error still exists.
To address this, we provide the LLM with the reason(Copy the prompt in 3.txt)
The revised code passes the syntax check and seems right.

## Slide 132: Testbench
Next, we'll modify the testbench to generate hex files containing matrix data. (Copy the prompt in 4.txt)
Finally, we incorporate a timeout mechanism and a cycle counter into the testbench (using the prompt from 5.txt).

## Slide 133: Kernel
To simplify the problem, we implement the kernel with combinational multiplier and memory first.
Compared to the testbench, the kernel's increased logical complexity needs more detailed prompts.
Copy the prompt in 1.txt

## Slide 134: Kernel
Define the Configuration, Interfaces and Memory Requirements as testbench

## Slide 135: Kernel
Supplement details regrading the operation flow
Provide an overview of the code structure

## Slide 136: Kernel
Copy the LLM’s output to gemm.sv
The code structure appears good but has several main issues
READ state computes multiplication
State Machine Behavior Issue
touch $REPOS/origen/gemm/kernel/gemm.sv

## Slide 137: Kernel
valid is a register but is updated in an always_comb block
Assignment Issue

## Slide 138: Kernel
The state transition logic for READ, COMPUTE,
and OUTPUT is incorrect.
State Machine Transition Issue

## Slide 139: Kernel
Send the prompt in 2.txt to fix them
State Machine Behavior Issue
Assignment Issue
State Machine Transition Issue

## Slide 140: Kernel
Some are fixed, but new ones emerge.
While the state transition logic of COMPUTE is now correct, the assignment of next_state inside the always_ff block is incorrect.
The assignment k <= k + 1 within the READ state is incorrect. To resolve this, either modify the COMPUTE state's condition from k < NK - 1 to k < NK, or relocate k <= k + 1 to the COMPUTE state.
Assignment Issue
State Machine Transition Condition Issue

## Slide 141: Kernel
The state transition logic for READ and OUTPUT is still incorrect.
Register is still updated in an always_comb block
State Machine Transition Issue
Assignment Issue

## Slide 142: Kernel
Send the prompt in 3.txt to fix them
Assignment Issue
State Machine Transition Condition Issue

## Slide 143: Kernel
Send the prompt in 3.txt to fix them
Providing reference code since the LLM didn’t fix them in the last attempt
Assignment Issue
State Machine Transition Issue

## Slide 144: Kernel
The LLM has made progress, but there are still a few errors.
In COMPUTE state, it forgets to reset k to zero when k achieves NK - 1
State Machine Behavior Issue

## Slide 145: Kernel
In COMPUTE state, it forgets to return to READ state
In OUTPUT state, it should return to READ state directly instead of waiting valid to be true
State Machine Transition Issue

## Slide 146: Kernel
Send the prompt in 4.txt to fix them
Provide the reference code
State Machine Behavior Issue
State Machine Transition Issue

## Slide 147: Kernel
Now we can run testbench to test it
It passes the test!
It takes 1089 cycles
  Average 2 cycles for each mac operation
cd $REPOS/origen/gemm
make gemm

## Slide 148: Add Single-cycle Latency Multiplier
Next, we’ll add the single-cycle latency multiplier to the gemm kernel
Copy the prompt in 5.txt
Give the requirements and multiplier definition

## Slide 149: Kernel
Seems good, it adds a MULTIPLY state to accommodate the latency
But it contains a silly error
It forgets to change the bit width
of state!

## Slide 150: Kernel
Send the prompt in 6.txt to fix it
Now we can run testbench to test it
It takes 1601 cycles
  Average 3 cycles for each
  mac operation
cd $REPOS/origen/gemm
make gemm

## Slide 151: Summary
Although the LLM may produce logic errors in the generated code, particularly in state machine.
LLMs demonstrate significant potential for accelerating hardware design.

## Slide 152: Thank you for listening!